## Slide 1: SnapSat
Critical Design Review
6th November 2015
Notes: Good Morning etc.

## Slide 2: Meet the Team
James Allworth – Attitude Determination and Control
Thomas Forbutt – Communications and On-board Data Handling
Oscar McNulty – Structural Design and Development
Penelope Player – On-board Computer and Power System
Nikita Sardesai – Thermal Control and Payload
Notes: First lets start by introducing the team. If you have any questions, feel free to ask.

## Slide 3: Our Mission
To bring space to YOU
Notes: So what’s out mission? SnapSat is destined to be a satellite that is directly accessible to you!
SnapSat is a nano-satellite designed for outreach and space accessibility for educational bodies and the general public. In a sun-synchronous orbit at an altitude of 350km, SnapSat will be in the prime position of Earth observation. Users can send a message to the cubesat, which will take beautiful images of the Earth and tweet it to the world.
SnapSat will relay position data, so users are able to take photographs where they please. There is also scope for the development of a desktop/phone application for direct user connection to the satellite via groundstation.
Following the success the final build and launch, the team is hoping to lunch SnapSat on a sounding rocket - where it will stay in a LEO for about 3 months, taking beautiful photographs!
For example (These are hypothetical and not images taken with SnapSat. However, these are indicative of the quality of photos we are hoping to achieve):
SnapSat will relay position data, so users are able to take photographs where they please. There is also scope for the development of a desktop/phone application for direct user connection to the satellite via groundstation.

## Slide 4: Design Point
1U Cubesat
$1000 budget
13 week timescale
Design for balloon launch to 30km
Communications: 5-node networking scheme
Figure 1 – Preliminary Design (this has since been improved upon)

## Slide 5: Operation Overview
Component Selection and Operation

## Slide 6: Component Selection

## Slide 7: System Interaction

## Slide 8: Structural Design
Oscar McNulty

## Slide 9: Final Design

## Slide 10: FEA Test Methodology
Natural Frequency
Sinusoidal Sweep
Random Frequency
Quasi-Static

## Slide 11: Mass Budget
Subsystem | Component | Mass + Contingency | Fraction of total mass
Structural | Chassis – Laser cut Aluminium Solar Panels | 435 g | 47.6%
ADCS | Air core coils (in house) Osram photodiodes Adafruit 9DOF IMU | 180.2 g | 22%
EPS | Batteries & Power bus | 122 g | 14.9%
OBC / OBDH | Arduino DUE board Memory storage | 31.2 g | 3.8%
TT&C | Antennae VHF/UHF receivers/transmitters | 84 g | 10.3%
Thermal | Heat taping, Kapton tape Multi-layer insulation | 4.8 g | 0.6%
Payload | TTL Camera | 25 g | 3.1%
Integration | Wires, bolts and cables | 9.5 g | 1.2%

## Slide 12: Mass Balance & Total Weight
Subsystem | Total Weight | Distance From Centroid | Inertial Contibution
Structural |  |  | 
ADCS |  |  | 
EPS |  |  | 
OBC / OBDH |  |  | 
TT&C |  |  | 
Thermal |  |  | 
Payload |  |  | 
Integration |  |  | 

## Slide 13: Attitude Determination and Control (ADCS)
James Allworth

## Slide 14: Attitude Determination
GPS
IMU
Sun Sensors

## Slide 15: Attitude Control
GPS
IMU
Sun Sensors
Magnetorquers
Control System

## Slide 16: Magnetorquer Design

## Slide 17: Control System Design

## Slide 18: Electrical Power System (EPS)
Penelope Player

## Slide 19: System Specifications
Components
Charging Circuit
Voltage Rails
Battery Lifetime

## Slide 20: Power Budget

## Slide 21: On-Board Computer and Data Handling (OBC/DH)
Penelope Player

## Slide 22: System Interactions

## Slide 23: Communications
Thomas Forbutt

## Slide 24: Components and Specifications
details

## Slide 25: Five-Node Network Setup
details

## Slide 26: Thermal Control
Nikita Sardesai
Note to snapsat: (this section is a bit too long – I will cut it down!)

## Slide 27: Space Thermal Dynamics
Model specified for 3 month, 350km orbit
Simplified mass: system dissipating heat to boundary exposed to space
General governing equation
Notes: Go though component selection
Note: we were able to achieve such a high mass budget since expesive, space rated and optimised componenet were selected.

## Slide 28: Space Thermal Environment
Notes: Go though component selection
Note: we were able to achieve such a high mass budget since expesive, space rated and optimised componenet were selected.

## Slide 29: Heat Transfer Modes
Heat flux relates to a change in temperature as
Three modes:
  Conduction
  Convection (not relevant)
  Radiation
Notes: Go though component selection
Note: we were able to achieve such a high mass budget since expesive, space rated and optimised componenet were selected.

## Slide 30: Total Incoming Radiation
Specification: sun-synchronous, 66% of orbit time spent in the sun, 98° inclination
  Simulated orbit was rotated 45° about the z Earth-body axis and 8° about the y Earth-body axis
Notes: Go though component selection
Note: we were able to achieve such a high mass budget since expesive, space rated and optimised componenet were selected.

## Slide 31: Total Incoming Radiation
Considering the external radiative fluxes
  Albedo (constant = 0.3), Solar (absorptivity = 0.8), Earth-IR. This is NOT panel-by-panel
Notes: Go though component selection
Note: we were able to achieve such a high mass budget since expesive, space rated and optimised componenet were selected.

## Slide 32: Panel Numbering
As a guide for the following slides
Notes: Go though component selection
Note: we were able to achieve such a high mass budget since expesive, space rated and optimised componenet were selected.

## Slide 33: Solar Radiation Per Panel
Notes: Go though component selection
Note: we were able to achieve such a high mass budget since expesive, space rated and optimised componenet were selected.

## Slide 34: Earth Infrared Radiation
Constant value for each panel throughout orbit
View Factor: projected visible area given by
Notes: Go though component selection
Note: we were able to achieve such a high mass budget since expesive, space rated and optimised componenet were selected.

## Slide 35: Earth Albedo
Albedo factor varies depending on the case considered
Notes: Go though component selection
Note: we were able to achieve such a high mass budget since expesive, space rated and optimised componenet were selected.

## Slide 36: Total Panel Incoming Radiation
Shown here for Panel 2, but computed for all panels
Notes: Go though component selection
Note: we were able to achieve such a high mass budget since expesive, space rated and optimised componenet were selected.

## Slide 37: Temperature Change Per Panel
To be completed
Notes: Go though component selection
Note: we were able to achieve such a high mass budget since expesive, space rated and optimised componenet were selected.

## Slide 38: Concluding Remarks

## Slide 39: Lessons Learned and Future Work
To be completed
Notes: Go though component selection
Note: we were able to achieve such a high mass budget since expesive, space rated and optimised componenet were selected.

## Slide 40: SnapSat
Critical Design Review
stemn.com/projects/cubesat-alpha